## Slide 1: Danfoss Visual Inspection System
Group DEC1704
Joey Elliott, Nick Gerleman, Cory Itzen, Evan Woodring
Advisor: Aleksandar Dogandzic
Sponsor: Danfoss Power Solutions

## Slide 2: Problem Statement
Detecting differences between assembled product and desired product using 3-D scanning
Detect defects
  Products are sometimes incorrectly configured
  Manual Inspection not always sufficient
Is this feasible with 3-D scanning ?

## Slide 3: Requirements
Functional
  Scan a real-world object
  Generate a 3D model of the object
  Compare scanned 3D models with existing CAD models
  Show users potential error locations in real-world objects
Non-Functional
  Complete the process in under a minute per real-world object
  Acceptable rate of false positives
  Be usable by employees without specialized knowledge

## Slide 4: Constraints and Considerations
Must work on existing assembly line
Real time
Ease of use

## Slide 5: Potential Risks
Real data vs synthetic data
Lack of information
Unknown performance

## Slide 6: Programming Languages and Tools
C++
Point Cloud Library (PCL)
  Eigen Math Library
Realsense SDK
Autodesk Inventor

## Slide 7: Overall System
Error Detection
Point Cloud Alignment
Surface Construction
3D Reconstruction
Mesh Extraction
Camera Capture

## Slide 8: Mesh Extraction
All possible components kept in a JT file
Need a mesh representation of the target product
Most standalone module

## Slide 9: Capture Module
Generate a 3D scan of the physical object
Two cameras tested
  Occipital Structure Sensor
  Intel RealSense

## Slide 10: RealSense Camera - Overview
Intel RealSense R200
Designed for Windows
Rear-mounted
Components:
  Conventional camera
  Infrared laser projector
  Infrared camera
  Microphone
Intel RealSense R200
http://reconstructme.net/wp-content/uploads/2015/11/r200.jpg

## Slide 11: RealSense Camera - How It Works
Laser Projection
  Project a known pattern
  RealSense sends grid of infrared light
Reading Infrared
  Distortion of pattern determines depth
Structure Light Scanning – Projector for laser patterns – Camera for reading
https://graphics.stanford.edu/papers/SpacetimeStereo/Princeton-TR-689-04.pdf

## Slide 12: RealSense Camera Scans

## Slide 13: 3D Reconstruction
Combine depth captures from multiple angles
Isolate distinct objects
Provided by RealSense SDK

## Slide 14: Surface Construction
Alignment and error detection are easier between point clouds
Mesh from CAD model describes polygonal faces
We need to build a point cloud from our mesh

## Slide 15: Mesh Filling Process
Process each face separately
Calculate area of triangle in 3D plane
Fill with random points of uniform density
time complexity

## Slide 16: Alignment Process
Orientation and scale of objects must match
Manually calibrating for alignment can be fragile
Align our points algorithmically using a point set registration algorithm
Point Cloud Library (PCL): Module registration
http://docs.pointclouds.org/trunk/group__registration.html

## Slide 17: Iterative Closest Point
Attempts to find “best” translation and rotation
Variants additionally support finding scale
Minimizes mean squared distance from point to closest reference
Active work area in our project

## Slide 18: Error Detection
Ideal Point Cloud
Physical Point Cloud

## Slide 19: Error Detection: Algorithm
Input: An Ideal point cloud "Ideal", and a scanned physical point cloud "Physical".
Output: A point cloud "Defects", containing all erroneous points in Physical
1. for each point P in Physical
2. find and record the distance from P to the nearest point in Ideal
3. calculate the outlier threshold T from the recorded distances
4. initialize an empty point cloud "Defects"
5. for each point P in Physical
6. if distance(P) > T
7. add P to Defects
8. return Defects

## Slide 20: Error Detection: Spatial Queries
KD Trees
Construction time:
Space
Nearest Neighbor:
KD-Tree
https://en.wikipedia.org/wiki/K-d_tree

## Slide 21
Chart: Squared Distance from Physical Point to Ideal Nearest Neighbor

## Slide 22
Chart: Squared Distance from Physical Point to Ideal Nearest Neighbor - Sorted
Interquartile Range = Q3 - Q1
= 23 - 7
= 16
Outlier Threshold = Q3 + 3 * IQR = 71

## Slide 23: Result

## Slide 24: Error Detection: Clustering
Actual errors consist of vertices clustered together
Points that are not clustered together are likely false positives

## Slide 25: Test Plan
Build synthetic objects to test
Create “Test Bench” to check integration
Test using real units at Danfoss facility

## Slide 26: Current Project Status
Appears feasible
Working prototype for most modules
Beginning integration

## Slide 27: Contributions
Joey
  Camera Capture and 3D Reconstruction
Cory
  Error Detection
Nick
  Surface Construction, Alignment, System Design
Evan
  Mesh Extraction and Camera Capture

## Slide 28: Plan for Fall
Team
  Prototypes during weeks 3 and 10
  Test with Danfoss products by week 8
Joey
  Camera Capture
Cory
  Alternate Error Detection Methods and Clustering
Nick
  Alignment and Test Bench
Evan
  Programmatically remove platform

## Slide 29: Questions